## Slide 1
Integration of GEO and LEO satellites
Integration of information from GEO(VIS/IR) and LEO (PMW) Satellites has been an active area of research.

## Slide 2
Using GEO satellites
(Infrared/Visible channels)
Advantage:
Good temporal and spatial resolution
(30 min or less, 4 km)
very good coverage
Disadvantage:
Receives mostly cloud –top information
Indirect estimation of precipitation.
Satellite precipitation retrieval instruments:
Satellite resources available for precipitation estimation

## Slide 3
2) Microwave
Advantage:
- Respond directly to hydrometeors and penetrates into cloud
- More accurate estimates
Satellite precipitation retrieval instruments:
Disadvantage:
- low temporal and spatial resolution (~5-50km)
Heterogeneous emisivity over land
(e.g., problem with warm rainfall over land)
2) Radar
Advantage:
More accurate
good space resolution
Disadvantage:
Very Poor temporal resolution
http://www.nasa.gov/mission_pages/hurricanes/archives/2005/h2005_gamma.html

## Slide 4
Precipitation sensors
Since 1979 we use satellites to estimate precipitation from space
Geostationary (visible/Infrared)
Microwave
Imagers
Microwave
sounders
Radars
DMSP (SSMI/SSMIS)
TRMM (TMI)
AQUA (AMSR-E
GPM (GMI)
NOAA/Metop
(AMSU/MHS)
TRMM (PR)
CloudSat (CPR)
GPM (DPR)
GPM
core
GPM
core
TRMM
Tropical Rainfall Measuring Mission
GPM
Global Precipitation
Measurement Mission

## Slide 5
Microwave temporal sampling
In Average ~ 80% global coverage between 50N-S every 3 hours
(Reference: Huffman et al. 2007)
Coverage every
½ hr.

## Slide 6
0.25°, 3-hourly
Non-trivial differences remain due to time-of-observation and sensor characteristics
00Z, 2 May 2004 S.E. of Sri Lanka
Courtesy of G. Huffman
Consistency among MW sensor precipitation

## Slide 8
+
-
-
+
+
T
T+3hr
T+6hr
T
t+3hr
Rain started between 3-hr period
Missed the peak
Rain ended between 3-hr period
Short-life event
Credit: K. Hsu et al.
Precipitation TEMPORAL resolution need for hydrology

## Slide 9
Flying/Planned/Expected PMW sensors
Equator crossing times (local)
PMW constellation continuity and crossing time aspects
Credit: Chris Kidd

## Slide 10
Tb (k)

## Slide 11
PMW Rain
observation
High-frequency
observation of cloud- top temperature & size
~ 3hr or more
We have no idea what is going to happen until next PMW overpass
Forward propagation of precipitation field
Cloud motion vector
Warm
Cold
REFAME:
Rain Estimation using Forward Adjusted Advection of Microwave Estimates
Cloud motion vector
0
1
2
3
4
5
6
7
Brightness temperature (Tb) feature
Mean rain rate for GEO-based cloud-classes obtained from long term GEO-LEO observations
Cluster
Mean rain rate
(mm/hr)
0
3
2
1
5
6
7
4
(Behrangi et al. 2010)
NASA Earth and Space Science (NESSF) fellowship
Notes: 11
11
This slide shows a concept to improve forward propagation of pmw rain estimation in time using
1) motion vectors obtained from cloud tracking algorithm of Tim Bellerby (2004), which gives a Lagrangian representation of cloud development. his algorithm provides a wind field and explicitly incorporates the effect of cloud growth, deformation and dispersal (decay)
2) Using the cloud classification techniques to classify different satellite pixels into number of distinct classes using extracted features
( such as temperature of the pixel, pixel’s textural properties (e.g., std & gradient) and also dynamic of cloud evolution using gradient of temperature in time between the same cloud pixel at two consecutive satellite imagery)

## Slide 12
Passive microwave sensors used in combined products during TRMM era
Global Operational REFAME
Every 30 min at ~ 0.08x0.08 deg. resolution
REFAME:
Rain Estimation using Forward Adjusted Advection of Microwave Estimates

## Slide 13
GOES-East TIR (Band 4)
Hurricane Georges,
17:02-17:15 GMT, 28th September 1998.
(above) GOES-East IR image for 17:02 GMT
(right) Forward displacement vectors, scaled to 40% of their true magnitudes
Cloud Advection Vector
Reference: Bellerby, TGARS, 2006
Tracking cloud movement using GEO IR Image

## Slide 14
MWadv
REFAME
COR compared to NEXRAD

## Slide 15
Behrangi et al. 2010
Case study

## Slide 16
/ra1/ali/test
Fundamentals of VIS/IR-based precipitation estimation

## Slide 18
Infrared (IR) Spectrum/Image

## Slide 19
Visible Spectrum/Image

## Slide 20
GOES-East - Regional sector view: Southern Plains

## Slide 21
GOES-East - Regional sector view: Southern Plains